## Slide 1: Chapter 6
Multiple Access Techniques for Wireless Communications

## Slide 2: Basic content
  Introduction
  Frequency Division Multiple Access (FDMA)
  Time Division Multiple Access (TDMA)
  Spread Spectrum Multiple Access
  Space Division Multiple Access (SDMA)
  Packet Radio
  Capacity of Cellular Systems

## Slide 3: Multiple Access Problem
The base stations need to serve many mobile terminals at the same time (both downlink and uplink)
All mobiles in the cell need to transmit to the base station
So we need multiple access scheme
  The idea behind the Resource Management in wireless communications was how to assign channels or frequencies to the radio cells in a way that the probability of interference is sufficiently low.
  The utilization of the capacity of a transmission medium can be improved through different methods that involved transmitting several connections simultaneously in a multiplex mode (Multiple Access Techniques).
  By using these techniques, the shared resource (spectrum) can be divided/shared among users, ensuring Quality of Service and the required amount of interference.

## Slide 4: Introduction
Multiplexing: is sending multiple signals or streams of information on a carrier at the same time in the form of a single, complex signal and then recovering the separate signals at the receiving end.
Multiplexing techniques are used to allow many users to share a common transmission resource.
In our case the users are mobile and the transmission resource is the radio spectrum.
Sharing a common resource requires an access mechanism that will control the multiplexing mechanism.

## Slide 5: Cont.
The goal of multiplexing is to share the medium with minimum interference and maximum medium utilization
As in wireline systems, it is desirable to allow the simultaneous transmission of information between two users engaged in a connection. This is called duplexing.
Two types of duplexing exist:
  Frequency division duplexing (FDD), whereby two frequency channels are assigned to a connection, one channel for each direction of transmission.
  Time division duplexing (TDD), whereby two time slots (closely placed in time for duplex effect) are assigned to a connection, one slot for each direction of transmission.

## Slide 6
Multiplexing in 3 dimensions
  time (t) (TDM)
  frequency (f) (FDM)
  code (c) (CDM)

## Slide 7: Frequency Division Multiplexing (FDM)
Separation of the whole spectrum into smaller frequency bands
A channel gets a certain band of the spectrum for the whole time
Each mobile (call) is assigned a separate frequency channel for the entire duration of the call
Sufficient guard band is required to prevent adjacent channel interference
Usually, mobile terminals will have one downlink frequency band and one uplink frequency band
Different cellular network protocols use different frequencies
Frequency is a precious and scare resource. We are running out of it

## Slide 8
Advantages:
  no dynamic coordination necessary, i.e., sync. and framing
  works also for analog signals
  low bit rates – cheaper
  No sensitive to propagation delay
Disadvantages:
  waste of bandwidth if the traffic is distributed unevenly
  inflexible
  guard bands
  narrow filters

## Slide 9: Time Division Multiplexing (TDM)
A channel gets the whole spectrum for a certain amount of time – orthogonal system
Advantages:
  only one carrier in the medium at any time
  throughput high - supports burst signals(like voice or speech )
  flexible – multiple slots
  Most suitable technique for digital transmission
Disadvantages:
  Framing and precise synchronization necessary
  high bit rates at each Tx/Rx
  synchronization is necessary

## Slide 10: Code Division Multiplexing ( CDM)
Each channel has a unique code
All channels use the same spectrum at the same time
Advantages:
  bandwidth efficient
  no coordination and synchronization necessary
  good protection against interference and tapping
Disadvantages:
  lower user data rates due to high gains required to reduce interference
  more complex signal regeneration